## Slide 1: TrioSim: a Lightweight Simulator for Large-Scale DNN Workloads on Multi-GPU Systems
Ying Li1, Yuhui Bao2,3, Gongyu Wang3, Xinxin Mei4, Pranav Vaid3,5, Anandaroop Ghosh3,
Adwait Jog6, Darius Bunandar3, Ajay Joshi3,7 and Yifan Sun1
1 William & Mary 2 Northeastern University 3 Lightmatter 4 Jefferson Lab
5 Stanford University 6 University of Virginia 7 Boston University

## Slide 2: Motivation
Large Workload
25000 A100 GPUs
GPT-4 network
90-100 days

## Slide 3: Motivation
GB200. Two GPUs, one CPU.
Large Workload
= 5 A100 GPUs

## Slide 4
Large Compute, Large Memory, Large Communication
GB200. Two GPUs, one CPU.
Large Workload

## Slide 5
Large Compute, Large Memory, Large Communication
GB200. Two GPUs, one CPU.
Large Workload
Simulators

## Slide 6: GPU Simulators
NVIDIA. (n.d.). GPU-Powered Simulation & Modeling. Retrieved from https://www.nvidia.com/en-us/high-performance-computing/simulation-and-modeling/"

## Slide 7: Simulation Performance
106X - 108X Slower
1 Second execution
  10 days – 2years
Simulation details
  Gate-level
  Cycle-level
  Instruction-level
Avalos Baddouh, Cesar, Mahmoud Khairy, Roland N. Green, Mathias Payer, and Timothy G. Rogers. "Principal kernel analysis: A tractable methodology to simulate scaled gpu workloads." In MICRO-54: 54th Annual IEEE/ACM International Symposium on Microarchitecture, pp. 724-737. 2021.
Simulation
Simulation
GPU time
GPU time

## Slide 8: Solutions
Simulate at a higher level of abstraction.
Operator-level traces from single GPU to simulate multiple GPUs execution.
TrioSim: Simulator for Large-Scale DNN Workloads on Multi-GPU Systems
https://www.nvidia.com/en-us/design-visualization/solutions/multi-virtual-gpus/

## Slide 9: TrioSim

## Slide 10: TrioSim

## Slide 11: TrioSim

## Slide 12: TrioSim

## Slide 13: TrioSim

## Slide 14: TrioSim
Trace Extrapolator
  Training parallelism
  Network structure
  Communication pattern

## Slide 15: TrioSim
Trace Extrapolator
  Training parallelism
  Network structure
  Communication pattern

## Slide 16: TrioSim
Trace Extrapolator
  Training parallelism
  Network structure
  Communication pattern

## Slide 17: TrioSim
Trace Extrapolator
  Training parallelism
  Network structure
  Communication pattern

## Slide 18: TrioSim
Trace Extrapolator
  Training parallelism
  Network structure
  Communication pattern

## Slide 19: TrioSim
Trace Extrapolator
  Training parallelism
  Network structure
  Communication pattern

## Slide 20: TrioSim

## Slide 21: TrioSim

## Slide 22: TrioSim

## Slide 23: MICRO 2023

## Slide 24: MICRO 2023
Layer or kernel execution times are generally linearly correlated to their Floating Point Operations.

## Slide 25: TrioSim

## Slide 26: TrioSim
1. Bandwidth 2. Latency
Total Transfer Time = Data Size/ Link Bandwidth + Link Latency
GPU
GPU
GPU
GPU

## Slide 27: TrioSim

## Slide 28: TrioSim

## Slide 29: TrioSim

## Slide 30: Experiment
Hardware.
P1: 2 NVIDIA A40 GPUs, connected with PCIe.
P2: 4 NVIDIA A100 GPUs, connected with NVLinks.
P3: 8 NVIDIA H100 GPUs, connected with NVLinks.
Software.
CUDA 12.1
Torch 2.1.0+cu121
Torchvision 0.16.0+cu121
Torchaudio 2.1.0+cu121
Workloads.
Image Classification: DenseNet, ResNet, VGG.
NLP: GPT-2, BERT-Base-Uncased, T5-Small, FLAN-T5-Small, and Llama.
Parallelism strategy.
Data parallelism, tensor parallelism, and pipeline parallelism

## Slide 31: Experiment
Data parallelism
Prediction errors comparing using TrioSim with applying distributed data parallelism on P1 and P2.
The average errors of the experiment set for P1 and P2 are 2.91% and 2.73%.

## Slide 32: Experiment
Tensor parallelism
Prediction errors comparing using TrioSim with applying Tensor parallelism on P1 and P2.
The average errors of the experiment set for P1 and P2 are 4.51% and 11.24%.

## Slide 33: Experiment
Pipeline parallelism
The prediction error comparing using TrioSim with applying pipeline parallelism on 4 A100 GPUs.
The average errors are 5.14%, 8.96%, and 8.18% for 1 chunk, 2 chunks, and 4 chunks, respectively.

## Slide 34: Experiment
New GPUs validation-----validate on P3, 8 H100 systems
Case 1 (cross-GPU prediction), input (1xA40 & 1xA100, BS128), output (8xH100, BS256);
traces from single A40 and A100 GPUs with a batch size of 128—
following Li’s model—to predict the performance on the 8 H100 system at batch size 256.
Case 2 (same-GPU prediction), input (1xH100, BS256), output (8xH100, BS256)
traces for a batch size of 256 on a single H100 GPU and use it as input of TrioSim to predict performance for the 8 H100 system.

## Slide 35: Experiment
New GPUs validation-----validate on P3, 8 H100 systems
Case 1 (cross-GPU prediction),
the average error is 9.09% for data parallelism, 9.07% for tensor parallelism
Case 2 (same-GPU prediction),
the average error is 6.69% for data parallelism, 9.09% for tensor parallelism

## Slide 36: Experiment
New GPUs validation-----validate on P3, 8 H100 systems
Case 1 (cross-GPU prediction),
the average error is 5.65%, 16.28% for pipeline parallelism with 1, and 2 chunks, respectively.
Case 2 (same-GPU prediction),
the average error is 4.20%, 13.76% for pipeline parallelism with 1, and 2 chunks, respectively.

## Slide 37: Use Cases
explore multi-GPU systems.
study high-level system behaviors,
e.g. parallelization strategies, network topologies, and scaling configurations.
combined with low-level simulators for architecture-level investigations.

## Slide 38: Limitations
Cannot evaluate fine-grained hardware modifications directly.
Accuracy drops when low GPU utilization limited by Li’s linear regression-based model.
Overlooks protocol-level and low-level communication effects.
Validation limited to CNNs and Transformers.

## Slide 39: Summary
TrioSim Lightweight
      Flexible
      Accurate

## Slide 40
TrioSim
Thank you!
Ying Li
Ph.D. Candidate
https://yingliphd.com
Scalable Architecture Lab

## Slide 41: Backup Slides

## Slide 42: TrioSim
Case A: only one message in the link.
A new message comes.
Routing, bandwidth allocation, and scheduling an event at the time, T1.
3) No new message comes, the destination device receives the message at the time, T1.

## Slide 43: TrioSim
Case B: two messages in the link.
4) Send the message to the destination. Routing, bandwidth allocation, and scheduling events at the time, T2.
5) A new message starts to transfer, and the current two messages share at least one link.
6) Recalculate the bandwidth and reschedule the delivery events of all the packets that are currently in transit at the time, T3 and T5 separately.
7) The destination receives the orange message at the time, T3. Because the orange message is received,
it recalculates the bandwidth and reschedules the delivery event for the blue message at the earlier time, T4.
8) The destination receives the message at the time, T4.

## Slide 44: Experiment
Pipeline parallelism
The prediction error comparing using TrioSim with applying pipeline parallelism on 2 A100 GPUs .
The average errors are 6.82%, 6.58%, and 15.10% for 1 chunk, 2chunks, and 4 chunks, respectively.
Orange triangle: an abnormal value contrary to the theoretical expectation that execution times should decrease with more chunks.

## Slide 45: Experiment
Communication & computation time
Communication and computation times for all the ATen layers of Convolution and Linear operations during the forward stage of VGG-11 training by tensor parallelism on P1.

## Slide 46: Experiment
Communication & computation time
Communication and computation time ratio for models training with tensor parallelism and data parallelism simulations on P1.